## Slide 1: MODELLING WATER QUALITY UNDER CHANGING CONDITIONS IN A NORDIC CATCHMENT
Csilla Farkas, Marianne Bechmann, Eva Skarbøvik
NIBIO, Norwegian Institute of Bioeconomy Research
Danube Conference 2019, Kyiv, Ukraine
6 November 2019.

## Slide 2
Norwegian Institute of Bioeconomy Research

## Slide 4: Challenges in implementing WFD in Norway
WFD
Eutrofication is usually the main cause for not fullfilling the requirements for good water quality in agricultural areas
  In South-Eastern Norway
  > 30% of the water bodies are characterized as being at risk or possibly at risk
  45% of the anthropogenic P input to Norwegian surface water originates from agricultural areas
  The natural background flux of P is estimated to be around 20-25% in the form of dissolved natural organic matter

## Slide 5
Water quality problems in the Nordic countries
freshwater ecosystems
marine ecosystems
Photo: E. Skarbøvik, NIBIO
An algal bloom in the Baltic Sea. satellite image: HZG
Baltic algae blooms in 2005. Photo: Kustbevakningen

## Slide 6
Extreme hydrological situations and soil loss
Photo: E. Skarbøvik, NIBIO
Photo: NIBIO

## Slide 7: Environmental monitoring program in Norway (JOVA)
JOVA started at the initiative of MOE, MOA and EPA-Norway in beginning of 90’s
JOVA: measurements runoff, nutrient and soil loss from agricultural dominated catchments under various cropping systems, climatic conditions, soil types and hydro-geological conditions
Discharge measurement (hourly)
Water sampling and analysis (SS, Ntot, Ptot, others )
Composite sampling approx. every 14 days

## Slide 8
Our main goals are:
To quantify the sources of soil particle and phosphorus losses
Identify possible cost-effective measures to reduce loadings of soil particles and nutrients under changing conditions

## Slide 9
Skuterud
Østensjøvannet
Årungen
Monitoring station
Skuterud catchment
Data since 1993
  Detailed data available on farm management practices
  Runoff, nutrient and soil loss
  Climatological data IMT, LMT
  Soil data available (S&L)
Total area: 4,5 km2
Arable land: 2,7 km2 (60 % of total area)
Forest: 1.3 km2 (31% of the total area)
Grain crops dominating (80-90 %)
Subsurface drainage system
  Spacing, L= 8 – 10 m
  Depth, d = 0.80 – 1.00 m

## Slide 10: The INCA-P model
INCA-P model:
    process-based
    semi-distributed model of the sediment and P transport in the
    dynamic catchment and river system
Catchment hydrology:
    direct runoff
    soil zone
    groundwater zone
INCA-P simulates at a daily time-step
    water flow and storage
    sediment and P loads from different land-use types
    in-stream SS, total, particulate and dissolved P concentrations

## Slide 11
  Parameterisation
    Available data from the Skuterud catchment and reach
    Literature review
    Expert assumptions
    Calibration procedure
    Stepwise calibration approach (flow; SS&TP)
    flow flow&SS&TP
    Validation procedure
    Scenario analyses
Application of the INCA-P model in the Skuterud catchment

## Slide 12: Application of the INCA-P model in the Skuterud catchment
  Warming up period: 1 September, 1993 – 31 December, 1993
  Calibration period: 1 January, 1994 – 31 December, 1999
  to set up the parameters for all the land use types
  Validation period: 1 January, 2000 – 31 December, 2007
  Land use types:
    Forest (31%)
    Grass (2%)
    Arable, No Autumn Tillage (18%)
    Arable, Autumn Tillage (41%)
    Urban (8%)

## Slide 13
Reference data for land-use specific sediment loss from

## Slide 14
Calibration period
Validation period
INCA-P model calibration results - hydrology

## Slide 15
INCA-P model calibration results – sediment and TP

## Slide 16
Yearly precipitation sum (mm)
Mean annual temperature (Co)
present
ICCP Project
Ensemble Project
KNMI
DMI
SMHI
Site-specific climate scenarios - selection
Reference period: 1930 - 1960
Study period: 2030 - 2050

## Slide 17
Simulated impact of the projected climate change in case of no change in present land use
Present climate
suspended sediment
TP
flow
C1 –C6: selected climate scenarios

## Slide 18
Implementing land use scenarios in the INCA-P model
Fertilisation ( 50 % increase/decrease)
Land use (crop field changed to a) grassland b) vegetables, c) forrest)
Soil management (different areal proportion of autumn and spring tillage; sawing and harvesting dates)

## Slide 19
INCA-P model: results for changes in land use / soil management

## Slide 20
Simulated impact of the projected climate change for present land use (REF) and two management scenarios (M1, M2)
suspended sediment
C0: present climate
C1, C4: selected climate scenarios

## Slide 21
Conclusions
The INCA-P model was capable to simulate the flow, sediment and P transport in the pilot catchment
It is important to use all the available expert-based information while calibrating simulation models (reference data for sediment losses from diff. land use areas in this case)
The land use / soil management scenarios, considered in this study can not mitigate the effects of future climate changes
Further efforts are needed to ensure good water quality in the future: Innovative measures for increasing water/soil retention in the landscape

## Slide 22
Extreme event
Forest
Stream
Rural areas
Urban solutions
Where can we apply measures?

## Slide 23
Measures in the forest

## Slide 24
Measures in rural areas

## Slide 25
Measures in the stream
Photo: E. Skarbøvik, NIBIO

## Slide 26
Measures to reduce peak flow and nutrient runoff
Water retention in the forest
Water retention ponds
Fertilization planning
Reduced tilling
Buffer strips
Grass covered waterways
Sedimentation ponds
Restauration of streams
Tile drainage maintenance
Measures for point sources
Land set aside as flooding area
Improved soil infiltration capacity
Photo: E. Skarbøvik, NIBIO

## Slide 27
Thank you for the attention!